Snake’n’Ladders

SWD GAMES LTD

UNIT 2 SANIGAR COURT

WHITTLE CLOSE

BRUNEL DRIVE

NEWARK

NG24 2DT

www.swdgames.co.uk

swd.leisure@yahoo.co.uk

TEL: 01636 708909

CONTENTS.

Copyright & warranty						page 2

Operating options						page 3

Set up procedure							page 4

Set up procedure							page 6

Play procedure							page 7

Control board menu						page 9

Parts list								page 11

Parts list								page 12

Parts list								page 13

Wiring/connectors  Mains/meters				page 14

Wiring connectors  Lamps/tickets				page 15

Wiring/connectors  Inputs/hopper/speaker		page 16

Wiring/connectors  Top box					page 17

Wiring/connectors  LED lighting				page 18

Wiring/connectors  outputs					page 19

Wiring/connectors 						page 20

COPYRIGHT

SWD Games LTD own exclusive copyright to the software contained within Alice’s Wonderland machine. Any purchaser of this machine have no authority to copy or reproduce this software or eproms unless granted prior permission in writing from SWD Games LTD.

SWD Games LTD retain intellectual rights to certain parts of this machine including SWD Games LTD processor boards and artwork, Patents are pending on artwork designs and may not be reproduced without prior permission in writing from SWD Games LTD Any person or persons wishing to make use of any parts of this machine should contact SWD Games LTD to obtain permission

WARRANTY

SWD Games LTD and or its distribution partners warrants that the following parts:

Power supply, Relay boards, microprocessor and motor

will remain free from defect if used correctly as deemed by SWD Games LTD

and the manufacturers for a period of 90 days from the point of purchase.

No other parts of the sellers within are warranted

Any warranted components as described which fail within the warranted period will be at the sellers sole liability repaired or replaced or credit the buyers account as long as the warranted parts are returned to the seller within the warranty period and returned prepaid by the buyer and after inspection that the said parts are free from neglect, alteration, misuse,accidental damage, improper repair or improper installation.

Only parts supplied or approved by the seller may be used within this machine.

In no event will the seller be liable for loos of profit, loss of use or incidental damage or consequential damages.

No employee of the seller has any authority to amend the details or terms of this warranty that shall be accepted by the purchaser on acceptance of the products referred to above.

OPERATING OPTIONS

PRICE OF PLAY

Current options available are 2p play, 10p play and 1 Euro play or operators tokens by prior arrangement.

The adjustment is made by changing the coin entry bezel to accommodate the desired coin.

Note: 1 Euro acceptance requires a modification to the pin panel, please call SWD Games LTD for guidance if this option is required.

SET UP/ PLAY PROCEDURE

Start up

Coin out version.

1. The machine will initialize with the solenoid in the closed position

2. Display glass lamps are off until the machine has fully initialized.

3. Motor will run.

4. All LED lighting will illuminate.

5. Attract sounds will play at factory set intervals, to adjust volume level a volume control is situated on the main PCB directly behind the coin out box.

Ticket only version.

- Hopper will run until empty.

- Machine glass lamps are off until machine has fully initialized.

3. Motor will run.

4. All LED lighting will illuminate.

5. Attract sounds will play at factory set intervals, to adjust volume level a volume control is situated on the main PCB directly behind the coin out box.

Set Up procedure.

After checking that the machine functions correctly the coin/token bed should be loaded with approximately 850 coins.

The first 700 coins can be placed directly onto the bed with the remainder being placed slowly at the bottom of the pin panel or being placed through the coin entries.

Counters.

Each coin passing a coin input switch will increment the coin in meter one position, Electronic meters are also held on the main pcb and can be accessed via menu button. (see section on program access)

Tilt.

A plumb bob tilt switch is located at the top behind the main pin panel and a vibration tilt switch is located on the right behind the bottom door, if either of these switches is activated an alarm will sound and if fitted a solenoid will activate for 15 seconds to allow coins to be diverted to the cash box.

Lighting.

All lighting within the machine is 12v ONLY. Any replacement lamps must be the same type.

Play procedure

- Cash in meter will increment 1 pulse per coin passing pin panel panel switch

- Coin in sound will play for each coin entered, assuming the previous sound sample has finished

- Cash payout bin will open via solenoid for 10 seconds

- Slam switch or tilt switch activation will immediately close the payout box solenoid and any coins paid over the edge riser will be diverted to cashbox

- Tickets will be paid randomly throughout game play

- Failure to pay a ticket will result in playfield red lamp flashing See error codes table

Error codes

Error lamp will flash as follows:

Tickets run out.

Illuminated name panel above meter door will flash continuously until tickets refilled and door is closed.

Closing door will result in machine paying out any tickets not previously paid out.

When tickets refilled any unpaid tickets will be dispensed on door close

SINGLE PLAYER PUSHER PARTS

METALWORK

| PART. |  |  |  | PART No. |
| --- | --- | --- | --- | --- |
| Coin Entry |  |  |  | 67.74.01 |
| Top Bed Plate |  |  | 67.74.02 |
| Reject Tray |  |  | 67.74.03 |
| Top Bed Under Tray |  | 67.74.04 |
| Meter Bracket |  |  | 67.74.05 |
| Lock Retainer Plate (Cabinet) |  | 67.74.06 |
| Lock Retainer Plate (Door) |  | 67.74.07 |
| Edge Riser |  |  | 67.74.08 |
| Pin Panel Under Channel |  | 67.74.09 |
| Door Switch Bracket |  | 67.74.10 |
| Top Bed Front Plate |  | 67.74.11 |
| Coffin Cover Side Plate RH |  | 67.74.12 |
| Coffin Cover Side Plate LH |  | 67.74.13 |
| Motor drive link With baring |  | 67.74.14 |
| Motor Mounting Plate |  | 67.74.15 |
| Ticket tray |  | 67.74.16 |
| Coin Entry Door Plate |  | 67.74.17 |
| Lightable Bottom Door |  | 67.74.18 |
| Solenoid Mounting Plate |  | 67.74.19 |
| Solenoid Cam |  |  | 67.74.20 |
| Solenoid Spring Arm |  | 67.74.21 |
| Door Payout Surround White |  | 67.74.22 |
| Payout tray |  | 67.74.23 |
| Halogen Lamp Holder |  | 67.74.24 |
| Relay Board Cover(Arduino) |  | 67.74.25 |
| Coin Chute |  |  | 67.74.26 |

| CABINET INTERNAL |  |  |
| --- | --- | --- |
| PART. |  |  |  | PART No. |
| Mains Harness |  |  | 67.74.501 |
| White Led Lighting |  | 67.74.502 |
| Blue Led Lighting |  | 67.74.503 |
| Sanken PSU |  |  | 67.74.504 |
| Busy B Microswitch |  | 67.74.505 |
| Slam Tilt Switch |  |  | 67.74.506 |
| Speaker |  |  |  | 67.74.507 |
| Tilt Wire L Bracket |  | 67.74.508 |
| Tilt Bob Wire |  |  | 67.74.509 |
| Tilt Bob O Bracket |  | 67.74.510 |
| Plumb Bob |  |  | 67.74.511 |
| 12 v Meter |  |  | 67.74.512 |
| 12v Led Halogen |  |  | 67.74.513 |
| Push/Pull Door Switch |  | 67.74.514 |
| Door Locks |  |  | 67.74.515 |
| Solenoid |  |  | 67.74.516 |
| Nylon Bars 8x8 |  |  | 67.74.517 |
| Nylon Bars 10x10 |  | 67.74.518 |
| Coin To Cashbox Tubes |  | 67.74.519 |
| Accurides |  |  | 67.74.520 |
| Motor |  |  |  | 67.74.521 |
| Cabinet |  |  |  | 67.74.522 |
| Carriage Of Parts |  |  | 67.74.523 |
| Fixing Screws |  |  | 67.74.524 |
| Top box light panel |  |  |  | 67.74.525 |
| solenoid |  | 67.74.526 |
| hopper |  | 67.74.527 |
| Arduino Sound Board |  | 67.74.528 |
| Sd Card |  |  |  | 67.74.529 |
| Amp Board |  |  | 67.74.530 |
| 9v Bard |  |  |  | 67.74.531 |
| Ticket dispenser |  |  | 67.74.532 |

| ARTWORK |  |  |
| --- | --- | --- |
| PART. |  |  |  | PART No. |
| Front Glass |  |  | 67.74.601 |
| Front glass decal |  | 67.74.602 |
| Top Box Panel |  | 67.74.603 |
| Pin Panel |  |  | 67.74.604 |
| Pin Panel cover |  | 67.74.605 |
| Pin Panel centre insert |  |  | 67.74.606 |
| Pin Panel RH insert |  |  |  | 67.74.607 |
| Pin Panel LH insert |  | 67.74.608 |
| Coffin Cover LH |  |  | 67.74.609 |
| Coffin Cover RH |  | 67.74.610 |
| Side panel top clear |  |  | 67.74.611 |
| Side panel bottom LH |  |  | 67.74.612 |
| Side panel bottom RH |  |  | 67.74.613 |
| Front door panel |  | 67.74.614 |
| Name panel (above door) |  |  | 67.74.615 |