Scissors Machine Specification

Accessories

- Keys

- Specification

- Power Line

- Micro-switch

Other

Motherboard Manuals

Motherboard Manuals

Motherboard Wiring Instruction

| The Count optical Sensor in front | The limit spacing optical Sensor in left | The Count optical Sensor in right |  |  | ground | ground | ground |  | 12V | 12V | 12V |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| The location optical Sensor in behind | The limit spacing optical Sensor in right | the limit spacing optical senor of scissor |  |  | ground | ground | ground |  | 5V | 5V | 5V |

| The motor of scissor | The motor of Before and after | The motor of left and right |  |
| --- | --- | --- | --- |
| The motor of scissor | The motor of Before and after | The motor of left and right |  |

| 12 V |  | 12 V | 12 V | 12 V | 12 V |  |  |  | ground | ground | ground | ground |  |  | light signal |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| into the table | out of the table | the button lamp |  | ground | ground |  | coin box | coin box | rocker arm | rocker arm | rocker arm | rocker arm | button | settings | test |  |

Motherboard Wiring Instruction

Motherboard Settings

Motherboard Settings

General Adjustment:

A1：How much coins once a game

A2：Game time

A3：Background music

A4：Shaking and distribution

A5：Music volume

A6：Bonus

the adjustment of scissors:

B1:the adjustment of scissors

B2:Before and after migration

B3:the winning position

Motherboard Settings

D Gifts Adjustment

D1:The ways of giving gifts

You can choose fixed mode,random mode and trafficking model to giving gifts

D2: X1 N once

D3: X2 N once

D4：x3 N once

D5：X4 N once

D6：X5 N once

D7：X6 N once

Check accounts

Total revenue（ do not reset）

Total gifts（ do not reset）

Current revenue

Current gifts

Machine fault maintenance

Machine fault maintenance

Machine fault maintenance

Machine fault maintenance

Machine fault maintenance

Machine fault maintenance

# Text boxes

Trumpet

Volume control

Motherboard electrial

interface

Contrast Ratio

Crown block motor

Special for factory

LCD

The test stopwatch of rocker button

Crown block signal

9 Test button(free play)

10

11 Always on when machine is running

12

13

14

15 Always on when machine is running

16 Always on when machine is running

Motherboard is in normal standby mode

Normal blinking

1

2

3 Rocker arm forward

4 Rocker arm backward

5 Rocker arm left

6 Rocker arm right

7 Scissors forward

8 Settings

1	2	3	4	5	6	7	8

9 10 11 12 13 14 15 16

J 5	the settings of Rocker,stopwatch and coin box

J 3	motor12 V

Please press the setting button under the normal initial screen ,so you can enter the setting main menu

You can select the option to through the rocker arm.

initial screen

地

- Check whether the optical senor is coming off

- Keep out the light and see if there is an indicator light on the main-board. If there is,proceed to step 3.if there is none,proceed to step 4.

- Check if the line is.if it is on,please replace new optical senor .if it is off,please proceed to step 4.

- Replace new main-board.

Liquid crystal display

1、Check whether the optical senor is coming off

2、Keep out the light and see if there is an indicator light on the main-board. If there is,proceed to step 3.if there is none,proceed to step 4.

3、Check if the line is.if it is on,please replace new optical senor .if it is off,please proceed to step 4、Replace new main-board.

1、check if the line is loose.

2、check if motherboard is connected.

3、contact related staff

1、check if the line is loose.

2、check if motherboard is connected.

3、contact related staff

1、Check whether the optical senor is coming off

2、Keep out the light and see if there is an indicator light on the main-board. If there is,proceed to step 3.if there is none,proceed to step 4.

3、Check if the line is.if it is on,please replace new optical senor .if it is off,please proceed to step 4.

4、Replace new main-board.